## Slide 1: Superpixel Classification
NeMo & NatureCoast
Bas Hoonhout & Max Radermacher, 12 December 2013

## Slide 2: Introduction
What do we see if we look at an argus image?
Image Classification
Sea
Beach
Dunes
Notes: What information do we use to classify these regions? A lot: shape, relative position, absolute position (when we have seen some Argus images before), color (something like HSV space), ‘texture’, …

## Slide 3: Introduction
What can we do with it?
Image Classification
Notes: Classification works in pixel space, but the results can easily be translated to x-y-space.
Shoreline mapper. By definition the interface between ‘beach’ and ‘sea’ is the shoreline. Elevation contour from tide + surge + wave set-up + wave run-up.
Intertidal beach detection. Potential source of sediment for aeolian transport.
Beach user detection. Pixels classified as beach users are mapped to x-y-space, yielding a surface area occupied by beach users. Establish a relation between surface and # of beach users (beach user density).
Two of these examples have already been applied in practice using highly specific detection algorithms. Superpixel classification is very general (can be applied for all methods) and is theoretically superior.
Probably many more applications, because it’s a very general method.

## Slide 4: Superpixel Classification
Segmentation (i.e. create superpixels)
Feature extraction Extract as much information as possible
Model construction and training Train a model which features characterize the classes
Model prediction Classify a new image
Overview of the method
Notes: What goes in is what comes out: the way you train the model, influences the predictions. Given the different purposes of classification (i.e. various tools), we want to settle on the best way to train.

## Slide 5: 1. Segmentation
Goal:
Clustering individual pixels, with similar intrinsic features, into n superpixels
Intrinsic features are related to:
Pixel intensity
  Value
  Spatial gradient
  Statistics of intensity (mean, variance, min, max)
Position (in m,n space)
Creating superpixels

## Slide 6: 1. Segmentation
N points are seeded in a regular grid
Around every grid point, pixels with similar features are sought
Free parameters:
Number of superpixels to create
Compactness (importance of Intensity vs. Position)
Various algorithms available
Notes: Point out the differences in behaviour. This becomes clear in each lower right side of the figures: the way the cross is incorporated.

## Slide 7: 1. Segmentation
Application to a Kijkduin image

## Slide 8: 1. Segmentation
Application to a Kijkduin image

## Slide 9: 2. Feature extraction
Extract as much information about the superpixels as possible:
Intrinsic features
Extracted features, e.g.:
  Area
  Area of convex hull
  Holeyness
  Shape
  …
Compute training data

## Slide 10: 2. Feature extraction
Compute training data

## Slide 11: 3. Model construction and training
A Conditional Random Field (CRF) is a type of Probabilistic Graphical Model (PGM)
A PGM is a graphical representation of a joint probability distribution:
Conditional Random Fields (CRF)

## Slide 12: 3. Model construction and training
Conditional Random Fields (CRF)
Vector with features associated with superpixel
Class associated with superpixel

## Slide 13: 3. Model construction and training
Conditional Random Fields (CRF)
C
f1
f2
f3
…
fK
Probability distribution for single superpixel over all classes and all possible states of feature vector
Probability distribution of a single feature
All superpixels share the same joint probability distribution

## Slide 14: 3. Model construction and training
Conditional Random Fields (CRF)
C00
f1
…
fK
…
f1
…
fK
C0M
f1
…
fK
…
f1
…
fK
…
f1
…
fK
…
f1
…
fK
CN0
f1
…
fK
…
f1
…
fK
CNM
f1
…
fK
A single joint probability distribution is associated with each superpixel in a regular grid
Class assignments only depend on features not on other superpixels

## Slide 15: 3. Model construction and training
Conditional Random Fields (CRF)
C00
f1
…
fK
…
f1
…
fK
C0M
f1
…
fK
…
f1
…
fK
…
f1
…
fK
…
f1
…
fK
CN0
f1
…
fK
…
f1
…
fK
CNM
f1
…
fK
Now the probability distribution for each superpixel over all classes and features also depends on class assignments of neighboring superpixels

## Slide 16: 3. Model construction and training
Conditional Random Fields (CRF)
C00
f1
…
fK
…
f1
…
fK
C0M
f1
…
fK
…
f1
…
fK
…
f1
…
fK
…
f1
…
fK
CN0
f1
…
fK
…
f1
…
fK
CNM
f1
…
fK
A potential node is added between adjacent superpixels limiting the dimensionality of the joint probability distribution
Ψ
Ψ
…
…
Ψ
Ψ
Ψ
…
Ψ
Ψ
...
Ψ
A potential is a dependent node without probability distribution that penalizes differences between adjacent superpixel assignments

## Slide 17: 3. Model construction and training
Conditional Random Fields (CRF)
Vector with features associated with superpixel
Class associated with superpixel
Pairwise potentials associated with neighboring superpixels

## Slide 18: 3. Model construction and training
Conditional Random Fields (CRF)
So we can read the thing we are interested in?
How do we determine this thing?
Model training

## Slide 19: 3. Model construction and training
A Conditional Random Field (CRF) is a type of Probabilistic Graphical Model (PGM)
A PGM is trained based on Bayes’ Rule for conditional probabilities:
Conditional Random Fields (CRF)

## Slide 20: 3. Model construction and training
Conditional Random Fields (CRF)
This is the thing we are interested in:
it gives the probability of each class to be associated with a superpixel given all features of that superpixel
A-priori probability distribution over feature values
A-priori probability distribution over classes
Counting classes
Counting features

## Slide 21: 3. Model construction and training
This is the thing we are interested in:
it gives the probability of each class to be associated with a superpixel given all features of that superpixel
A-priori probability distribution over feature values
A-priori probability distribution over classes
Counting classes
Counting features
Conditional Random Fields (CRF)
Probability distribution over feature values given the class of the superpixel
Counting features per class
We need feature values that are associated with a pre-determined number of classes

We need manually classified images!

## Slide 22: 3. Model construction and training
Now we can extract the conditional probability distribution from manually classified images:
An iterative optimization algorithm can subsequently provide us with the largest joint probability and hence the most probable classification of the image:
Conditional Random Fields (CRF)

## Slide 23: 3. Model construction and training
Example: beach user detection algorithm
Dimensionality

## Slide 24: 3. Model construction and training
1-dimensional discrimination
Threshold set by manual calibration
Dimensionality
Pixel intensity
0
Beach
Object

## Slide 25: 3. Model construction and training
Example: shoreline mapping
Dimensionality

## Slide 26: 3. Model construction and training
Example: shoreline mapping
Dimensionality

## Slide 27: 3. Model construction and training
Example: shoreline mapping
Dimensionality

## Slide 28: 3. Model construction and training
What about superpixel classification?
Every feature adds a dimension
The analysis is 50-70 dimensional!
Segmentation has yielded many additional features to examine
Dimensionality

## Slide 29: 4. Model prediction
Evaluate the n-dimensional classification space for the new feature values:
Classify a new image

## Slide 30: Training dataset
Training is a trade-off:
Having a lot of classes leads to small differences between classes
  Dunefoot vs. beach
  Intertidal beach vs. dry beach
Having too few classes does not provide enough detail
  If you only classify ‘off-shore’ and ‘onshore’, you cannot compute the surface of the beach, or detect beach users
Issues
This is confusing!

## Slide 31: Training dataset
Being very strict in the way you classify (no ambiguity)
Defining an optimal amount of classes
Introducing a two-step method
  Coarse classification: sky, sea, beach, dune, objects (, labels)
  Fine classification: Beach = {people, intertidal, …} Dune ={sand, vegetation, pathway} …
Solution